## Slide 1
LAN (Local) => one site (one physical network topography)
  Classroom is an example of LAN, connecting computers together
WAN (Wide) => multiple sites (need employ router/link)
  Internet is an example of WAN, connecting lots of LAN together
Mostly used service is LAN
  我們從家中連上Internet, 也是先連上ISP的LAN
Extranet: outer public subnet
Intranet: inner private subnet
Network Structure

## Slide 2
Network Topography (2 types)
Physical Topography => describe the real network connection configuration between nodes (連線部屬的配置)
  Bus : no Hub, packet are transmitted through node to node (一節點壞掉會影響其他節點, 除錯困難)
  Star : hub in center to control transmit. Use different port in hub to connect (傳送/除錯/佈線皆方便)
  Ring : no Terminator (佈線困難)
Logical Topography => describe how data message are transmitted (訊息傳送的方式)
  Ethernet : broadcast message and every node will check destination to read or deliver (同時廣播會碰撞)
  Token Ring : token packet dedicated, token will authorized node to send message (拿到token packet才可以講話)
Combination of Physical / Logical Topography
  Bus / Ethernet : mostly used for LAN
  Star / Token Ring

## Slide 3
Hardware
Network Interface Controller, NIC (網路卡)
  Different logical topography require different NIC (e.g. 10/100 Ethernet)
  Each NIC contains 48bits NIC MAC address to recognize (網卡IP位址)
Cable and Head (網線/接頭)
  Twisted Pair Cable and RJ45 head (雙絞線/RJ45接頭): commonly used
  Coaxial Cable and BNC (同軸線/BNC接頭)
  Fiber Optic Cable

## Slide 4
TCP/IP and OSI model
TCP/IP (Transmission Control Protocol and Internet Protocol)
  Protocol that connected different network system together
  Based on OSI model with 7 distributed layers with separated function
    Physical: 傳送訊號的硬體配置(裝置, 佈線, 網路型態), 配置不同 (Ethernet or Token Ring), 實體層就不同
    Data Link: 基本的傳送訊號單位(frame), with MAC address, 制定傳送規則(配合不同實體層)與錯誤檢測來確保物理傳輸順利
    Network: 分析起迄節點IP, 依交通狀況決定路徑 (流量控制)
    Transport: 將資料切割成小封包(單位傳輸量有限), 制定傳輸順序/檢測方法, 目的地節點才能正確讀取 (決定用TCP or UDP)
    Session: 建立連線請求/結束請求
    Presentation: 針對不同的節點中的硬體架構做字元編碼/資料型態轉換, 方便應用程式讀取
    Application: 針對應用程式的不同需求(htp/htp/ssh.etc) 進行檔案格式轉換
Data Transmitting (封裝 -> 傳送 ->拆裝)
  Each layer will process separately by adding header
TCP: connection and reliable transmission
UDP: connectionless but faster

## Slide 5: Encapsulation (封裝) and Decapsulation (拆裝) 1. Data message begins from application layer, e.g. FTP/mail/http.etc request 2. As going through layers, Each layer will append header message (Ht/Hn/HI) 3. Intermediate like switch/router will decapsulate and read message according to layers 4. Switch is layer 2 device, only read HI data and generate new HI for next link layer. (網卡IP) 5. Router is layer 3 device, will read Hn (Source/Destination IP) and decide route
message
segment
datagram
frame
source
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn
Hl
M
router
switch
data
Transmission Example (Five layers instance)
header
Switch => layer 2
Router => layer 3
封裝
變大
拆裝變小
讀header message
封裝
新的Link
新的HI
Data from different layers
Application => Message (最初的data, reliable 不容許遺失)
Transport => segment (header Ht => TCP/IP hand-shaking message)
Network => datagram (考慮 Source/Destination, Hn => ip 32 bits addr)
Link => frame (考慮node to node, HI => node to node 網卡ip 48bits)
data

## Slide 6
Transmission Example (Post system example)
http://www.pcnet.idv.tw/pcnet/network/network_ip_model.htm

## Slide 7
Internetworking equipment (Connecting LANs)
Layer 1 Devices ( Physical layer : with no directory function)
  Repeater (增益器): to repeat and enlarge signal from loss during long distance transmission (bus topography)
  Hub (集線器): hub in center as connection service main node and repeater (broadcasting in star topography)
Layer 2 Devices (Link layer : check MAC address)
  Bridge (橋接器): filter function (receive -> check -> decide if send to another segment) (bus topography)
  Switch (交換器): filter function (center receive -> check -> send to target node) (star topography)
Layer 3 Devices (Network layer : check IPs)
  Router (橋接器): with source / destination IPs, connecting LANs and routing decision. (Gateway service)
LANs
Internet

## Slide 8
LAN and Internetworking
Hub (layer1) with no directory function only broadcast the received packet data ( cause extra traffic loss)
Switch (layer2), based on MAC address, will send the received packet data to target node in LAN
https://www.youtube.com/watch?v=1z0ULvg_pW8&t=187s

## Slide 9
LAN and Internetworking
Router (layer 3) will recognize IP and decide the route to send packet to the other LAN
In LAN transmission, packets are usually handled by layer2 switch
Network transmission need Router to involve (sometimes layer3 switch)
https://www.youtube.com/watch?v=1z0ULvg_pW8&t=187s

## Slide 10
IP => 32bits binary code
Class (A,B,C)
127: for local test
127.0.0.1 => localhost

## Slide 12
SSH (secure shell)
ssh remote connection
  with user name / passwd
  with keys
    Public key (鎖頭, 放在server的路徑:~/.ssh/authorized_key)
    Private key (鑰匙, 本機保留)
Connection with private key : ssh –i (私鑰位置) ec2-user@ip4
Connection without private key : 要把私鑰放到正確路徑, 讓系統自動抓取
  路徑 : 本地端: ~/.ssh
  可以自動抓取的名字 : identity/id_rsa/id_dsa
Need to check folder accessibility: chmod 700 ~/.ssh
localhost
server

## Slide 13
HTTP
Client / Server (request/response)
Stateless (each transaction is independent) => how to
Application layer